## Slide 1: Some Lessons from History
Ross Callon (retired)
(& John Scudder, Juniper)
IETF 102, Montreal
July 2018

## Slide 2: Lessons from History
There have been major Internet issues
  “Interesting” events in 1980’s, 90’s, 200x’s
  We didn’t always know what we were doing
Some knowledge is in the mind of old folks
I thought it would be wise to write some of these down
Examples to follow
  I have tried to be fully vendor-neutral (eg, have not considered issues with proprietary protocols)

## Slide 3: Arpanet Collapse (early 1980's)
A switch crashed and restarted
  Forwarded old packets in output queue
Result: Old Route Update was propagated…
  While another update was in progress
  Old update was exactly 1/2 way around circular sequence space (a>b; b>c; c>a)
  Update A replaced Update B
  Update B replaced Update C
  Update C replaced Update A…

## Slide 4: Arpanet Collapse (early 1980's)
Problem: Three updates chased each other around the Arpanet for hours
Solution: All but two packet switches had to be manually shut down
(today, with hundreds of routers per network, this could be quite unpleasant)

## Slide 5: OSPF Flooding Issue (early 1990’s)
Stable Network, Well-connected core with single-homed stubs
S.P. thought: I really care about reliability. Let's multi-home stubs…

## Slide 6: OSPF Flooding Issue…
Redundancy added:
Result: Collapse
What happened?

## Slide 7: OSPF Flooding Issue…
Core router had LSA to send out
  Transmitted to all adjacent routers
Stub routers all forwarded the LSA to their neighbors…
LSAs

## Slide 8: OSPF Issue…
Result: Other core router was overwhelmed with LSAs forwarded by stub routers
Lesson: Buffering and discarding duplicate LSAs is a difficult part of OSPF/IS-IS
  No one predicted this
LSAs

## Slide 9: Flooding Issue with IP over ATM
Similar issue occur with full mesh of circuits over an ATM core
Mesh groups added to deal with this

## Slide 10: Lost Hellos (~1992)
Network stable for long periods of time
Multiple random changes in short order cause processor to fall behind
  Processor drops Hellos, adjacencies dropped
  More routing updates transmitted
  Widespread CPU congestion, more Hellos dropped
  Entire network disconnects
  Problem stabilizes, network recovers
  ~20 minutes later, many LSAs are refreshed, problem repeats

## Slide 11: Lost Hellos…
Solution
  Optimize protocol processing
  Prioritize Hello processing
  Randomize timers
  (Apply to all routing protocols)
This was known in early 90's
But…

## Slide 12: ATM Switches, mid 1990's
ATM Network partitions, re-connects
New updates flooded between partitions
CPUs congest, drop Hellos
Adjacencies dropped, Network Disconnects
('Prioritize Hellos' wasn't well enough known)

## Slide 13: IP Nets: DDoS Attacks
Attacker compromises many hosts, uses them to launch a coordinated attack
Result: Link Congestion
Attacker
Attacker
Attacker
Victim

## Slide 14: Slammer, January 2003
Slammer worm
  Very rapid propagation (doubles in ~8sec)
  Widespread congestion in IP networks worldwide
Result
  Routers drop Hellos, Adjacencies dropped
  Network disconnects
  (not clear if result of link or CPU congestion)
  Issue getting management plane to respond

## Slide 15: Solution: Prioritize Hellos + …
Give priority, guaranteed resources for real time protocol functions
Prioritized queues
  Inside router, and on egress

## Slide 16: Invalid Update Issue
IS-IS (and OSPF) defined in mid 1980's
  Smaller CPUs, which also forwarded packets
   Original spec minimizes CPU strain
  In forwarding IS-IS updates: Check outer wrapper, forward, then check internals
IS-IS & OSPF were widely deployed, interworked well
  IS-IS was solid for several years

## Slide 17: Invalid Update Issue,…
Bad interface trashes update
  One in ~65,000 have checksum which passes
  Check outer wrapper (OK)
  Forward (OK)
  Check internals: Field out of range, Crash
Result: Entire area crashes
  Many rtrs, multiple vendors

## Slide 18: Distance Vector (RIP) Count to Infinity
Distance vector count to infinity is fairly well known
A
“A one hop”
“A two hops”
“A two
hops”
“A three
hops”
“A three
hops”

## Slide 19: Distance Vector (RIP) Count to Infinity
Many fixes have been proposed, some deployed
There was an interesting “augmenting” to this problem in the early NSFnet…
A
“A two hops”
“A four
hops”
“A three
hops”
“A five hops”
“A six
hops”

## Slide 20: Delay Based Routing
There have been multiple “interesting” experiments with routing based on real time (queuing) delay
Early NSFnet “Fuzzball” routers had delay based “Hello” protocol in the core, mapped to RIP around the edges
  Delays vary dynamically, feeding unstable metrics into RIP
  This was not pretty
An Arpanet variant used a linear combination of hop count and real time delay, carefully overdamped
  When delays grew (congestion), it became under-damped

## Slide 21: Non-deterministic routing
”BGP wedgies” are a well-documented example.
One set of policy configurations can result in multiple different stable forwarding topologies (“multistable”), depending on timing.
  Because policies are local, but forwarding is global.
Much more detail in RFC 4264.

## Slide 22: BGP “wedgies” simple example
C uses BGP community to tell X “use this link as a last resort only”
When primary fails, all is well.
But when primary is restored, forwarding topology has a new stable state. (And not what C intended.)
primary
backup
Customer C
Provider X
Provider Z
Provider Y

## Slide 23: BGP MED Oscillation
Actually, BGP isn’t even always multistable.
The BGP MED path attribute can cause persistent oscillations (see RFC 3345).
How did this happen?
  BGP route selection assumes total order.
  MED gives only a partial order (MED is only comparable if source AS is the same).
Protocol was designed to be correct with a flat IBGP
  MED wasn’t considered when designing route reflection, which does data hiding.
  Even if it had been, not clear there would have been a solution.

## Slide 24: Optional Transitive BGP Attributes
Some BGP data is opaque to routers handling it, and can transit across them.
  Optional Transitive Path Attributes, most famously.
When the data is handled by a router that does understand it, the router says “oh my goodness my peer has sent me a bad update it must be insane” and resets the session.
  But the peer didn’t misbehave. Some router far across the Internet did.
  This means one naughty router can cause a very large number of sessions to reset.
Best intentions by protocol designers, but a terrible outcome.
Fixed by RFC 7606 (keep the session up but delete the malformed routes, don’t assume the peer has gone insane).

## Slide 25: BGP – a few lessons
Simple protocols have complex behaviors when assembled into large systems.
Extensible protocols lead to small extensions that have surprising consequences when they interact.
If you serve several masters (protocol correctness, business reality) something has to give.
Data that is sometimes opaque leads to results that are sometimes surprising.
The worse-is-better design philosophy is powerful.

## Slide 26: Other examples…
Operator errors
Distribution of full BGP routes into IGP (IS-IS, OSPF, …)
Scaling
Signaling System 7 (SS7) failure
Rumors of other issues
And note, I have not mentioned multicast…
  Eg, “multicast grenades” are in principle possible

## Slide 27: What To Do With This Information?
I had been intending to write an Internet Draft (to RFC)
  This isn’t going to happen (I am retired, and like it that way)
  Adding more detail and additional examples would be useful
“Those who cannot remember the past are condemned to repeat it”
  Old saying (possibly originally by George Santayana)
Today, repeating these failures is not acceptable
  We all depend upon a stable and reliable Internet
Hopefully, this presentation can be helpful